Solar Fountain

Instruction

Model No. GY-D-005S

Product Introduction

This product is solar-powered decorative fountain. It is made up of highly efficient solar panel and new brushless pump. It is start-up fast, efficient and strong stability. In addition, it has no electric outlet or external battery, so it’s not only easy to use, but also safe. This product is suitable for bird bath, fish tank, small pond, garden decoration, water circulation for oxygen, etc.

Product Specification

- Solar panel: 12V/5W

- Brushless pump input: DC 6-12V

- Maximum quantity of flow: 380L/h

- Maximum delivery head: 120cm

Product Performance

- Maximum water height: 60cm

- The pump will start automatically in 3 seconds when bright sunlight shines on the solar panel directly without any shadow.

Method of Operation

1. Assemble the product according to the sketch map.

2. Set it on the places where the solar panel is not sheltered from the sun. Then it will work normally as soon as the sunshine is enough.

3. There is some air in the pump at the moment that it is put in the water. You’d better not connect the spray head to the pump until it sprays normally.

Note

1. The pump is driven directly by the sunlight. So it will work continuously only when the sunlight is enough. As the power of the solar panel is depended on the sunlight, the pump is also affected by weather, seasons, places, etc.

2. Don’t make the pump work without water for a long time, or its lifespan will be shortened.

3. Don’t put the solar panel and the control box in water, or it will be damaged.

4. Clean the pump regularly. If it’s duty, it will stop working.

5. The solar panel is made up of glass and metal. You must be careful when using it. And don’t let children play with it.